## Slide 1
Project
Characterization techniques applied to the thesis: Evaluation of triborheological systems with medical applications
Laura Catalina Duque Ossa – A01747663
F
I
N
A
L

## Slide 2
Agenda
General description of the thesis and the importance of characterization techniques to evaluate results.
Introduction
01
Explanation of 6 techniques that allows to evaluate different characteristics inside the research.
Characterization Techniques
02
Positive effect of the techniques on the research.
Summary
03
Questions and answers from professors and students.
Q/A
04
FINAL
Project

## Slide 3
Porosity, surface distribution, wear tracks and performance.
Importance of characterization techniques
Synovial Joints of the human body
Mechanical system
Degenerative condition of synovial joints
Osteoarthritis (OA)
Polymeric hydrogels (polyvinyl alcohol - PVA)
Cartilage Replacement
Fluids with additives (Hyaluronic acid - HA with mesoporous silica nanoparticles – SiMNP’s)
Lubricants
INTRODUCCTION
Thesis Description

## Slide 4
2
3
4
1
Scanning electron microscopy (SEM)
Porosity
Surface distribution
Wear tracks after triborheological tests
Nanoparticles distribution in the lubricant
Sample preparation
General description
Dry sample with conductivity properties. Coating with a tiny film of gold
A beam of electrons scans across the material surface, producing high-energy back-scattered electrons, low-energy secondary , auger electrons and cathodeluminescence. The back-scattered electrons provides a physical image of the surface whit their analysis
Chen et al., "Preparation and property of high strength and low friction PVA-HA/PAA composite hydrogel using annealing treatment “, Materials Science and Engineering C, vol. 91, pp. 579 – 588, 2018.
Maiolo et al., "Development and characterization of Poly (vinyl alcohol) based hydrogels for potential use as an articular cartilage replacement“, Materials Science and Engineering C, vol. 32, pp. 1490 – 1495, 2012.
Li et al., "The Effects of Surface Mechanical Deformation and Bovine Serum Albumin on the Tribological Properties of Polyvinyl Alcohol Hydrogel as an Artificial Cartilage “, Advances in Materials Science and Engineering, pp. 1 – 10, 2017.

## Slide 5
SEM derivation
Environmental scanning electron microscopy (ESEM)
Maintain the natural hydrated state of the sample without additional preparation
Uses
Pores, wear and cracks
Wet-mode
Li et al., "Influence of dynamic load on friction behavior of human articular cartilage, stainless steel and polyvinyl alcohol hydrogel as artificial cartilage“, J Mater Sci: Mater Med, vol. 21, pp. 147 – 154, 2010.

## Slide 6
Atomic force
Microscopy (AFM)
A laser beam is reflected from a cantilever that has a tip (probe). As the tip approaches the sample, the cantilever experiments deflection towards or away from the surface, causing changes on the reflection of the detected beam. The changes are detected by a photo-diodo while a piezo scanner moves the tip over the sample.
Sample preparation : Hydrated state, tapping mode, distilled water, 37°C.
Use : Visualization of nano-roughness after test.
Shang, Yuping and Wang, Hongda, “The structure and function of cell membranes examined by atomic force microscopy and single-molecule force spectroscopy”, Chemical society reviews, vol. 44, pp. 3617 – 3638, 2015.
*
*
Sardinha et al., “Tribological characterization of polyvinyl alcohol hydrogel as substitute of articular cartilage”, Wear, vol. 301, pp. 218 – 225, 2013.

## Slide 7
01
02
Distilled water, low scan rate (10°C/min), nitrogen atmosphere, 40 – 250 °C
Sample preparation
Change in water content (hydrophilic behavior)
Uses
Peak temperature values (Support at body temperature)
Simple Portfolio Presentation
Differential scanning calorimetry (DSC)
Measurements of thermodynamic properties (heat capacity) of thermally induced transitions, applied to a variety of biological elements such as biopolymers. During experiments, parameters like post scan temperature, the number of scans, their range, scan rate, and feedback strength are important and can be changed to obtain the best results.
Polymer science learning center, “Differential scanning calorimetry”, 2019.
Echeverri et al., “Síntesis y caracterización de hidrogeles de alcohol polivinilíco por la técnica de congelamiento/descongelamiento para aplicaciones Médicas”, Revista EIA, vol. 12, pp. 59 – 66, 2009.

## Slide 8
Work with metal slide at a excitation of 785 nm
Sample preparation
See variations in the fluid structure after the addition of nanoparticles.
Use
Raman spectroscopy
Recompile knowledge about molecular information (functional groups) and crystalline structures. A laser irradiate the sample with monochromatic radiation, with excitations in the UV, visible and near-IR spectral region (785-1064nm). The irradiation generates a Raman scattered light (spectrum) that is detected with a camera.
Wu et al., “In vivo lipidomics using single-cell Raman spectroscopy”, PNAS, vol. 108, pp. 3809 – 3814, 2011.
Baia et al., “Discrimination of Human and Nonhuman Blood by Raman Spectroscopy and Partial Least Squares Discriminant Analysis”, Analytical letters, vol. 50, pp. 379 – 388, 2017.
Kim et al., “Effect of pH on Swelling Property of Hyaluronic Acid Hydrogels for Smart Drug Delivery Systems”, Journal of Sensor Science and Technology, vol. 21, pp. 256 – 262, 2012.

## Slide 9
Thermomechanical analysis (TMA)
Changes in a dimension of a sample as a function of temperature, time, force and atmosphere . Force can be applied in compression, tension, flexure or torsion modes using different probes (quartz glass, silica, alumina and metals)
Sample preparation
Use
Smooth, less of 10mm of height, silica probe, heating rate of 5k/min, nitrogen atmosphere, ramped force
Mechanical properties of the hydrogel at body conditions (Elastic modulus – 0.45 a 0.8MPa)
Hitachi, “Principle of Thermomechanical Analysis (TMA)”, 2019

## Slide 10
The Summary
Characterization techniques in medical applications
Challenges of joint replacement processes
Study of synthetic articular cartilage and lubricant with nano-additives
Wear, composition, porosity and performance
Mechanical properties that gide the applications
Morphology
Properties
Elemental
Composition
Application
2
1

## Slide 11
Thank You
Q/A
Characterization of materials
F
I
N
A
L
P
r
o
j
e
c
t