## Slide 1: 2_Class Activity 06.07.2020 Case 2B-3 : Team5
Javid Azimi Boulali <A00829592@itesm.mx>
Antonio Osamu Katagiri Tanaka <A01212611@itesm.mx>
Julio Alberto Cao Romero Gallegos <A01327704@itesm.mx>
Bryan Iván Quintanar Abarca <A01751178@itesm.mx>
07 Jul 2020

## Slide 2: Phenomenon and Problem Explanation
[1] Y. X. Chen, B. Cain, P. Soman, Gelatin methacrylate-alginate hydrogel with tunable viscoelastic properties, AIMS Mater. Sci. 4 (2017) 363–369. https://doi.org/10.3934/matersci.2017.2.363.
The objective of adding alginic acid to gelatin methacrylate (GelMA) is to modify its viscoelastic property to mimic an extracellular matrix prone to the study of living cells interactions.
The researcher wants to use alginic acid as an additive to modify the elasticity of GelMA and produce methacrylate-alginate (Gel-Alg). A major problem would be the lack of compatibility of both materials, resulting in compromised properties such as: thermal stability or even chemical stability.

## Slide 3: Available Information & Assumptions
[1] Y. X. Chen, B. Cain, P. Soman, Gelatin methacrylate-alginate hydrogel with tunable viscoelastic properties, AIMS Mater. Sci. 4 (2017) 363–369. https://doi.org/10.3934/matersci.2017.2.363.
Results obtained from creep and compressive tests reveal that the alginate component of Gel-Alg composite, can be effectively crosslinked, un-crosslinked and re-crosslinked by adding or chelating calcium ions.
Polymers use a combination of strong permanent crosslinks and weak bonds that could reversibly break and re-form, to generate a viscoelastic response.
Ions (CaCl2) solution was used to ionically crosslink the alginate component of the UV-crosslinked composite affecting insignificantly its mechanical properties. Alginate acts as the dynamic modifiable element controlled by ionic non-covalent bonding in the presence of calcium divalent ions, while GelMA acts as a stable structural element.
In Gel-Alg, the re-crosslinked states exhibit similar viscoelastic properties to the crosslinked state, confirming that
crosslinking is reversible and this process is capable of dynamically controlling the elastic recovery

## Slide 4: Solution & Justification
[1] Y. X. Chen, B. Cain, P. Soman, Gelatin methacrylate-alginate hydrogel with tunable viscoelastic properties, AIMS Mater. Sci. 4 (2017) 363–369. https://doi.org/10.3934/matersci.2017.2.363.
[2] R. Kadri, J. Bacharouch, K. Elkhoury, G. Ben Messaoud, C. Kahn, S. Desobry, M. Linder, A. Tamayol, G. Francius, J.F. Mano, L. Sánchez-González, E. Arab-Tehrany, Role of active nanoliposomes in the surface and bulk mechanical properties of hybrid hydrogels, Mater. Today Bio. 6 (2020) 100046. https://doi.org/10.1016/j.mtbio.2020.100046.
Addition of alginate within GelMA exhibits varying degrees of viscoelasticity depending upon the amount of alginate in the composite. The increases in elasticity of the solution is caused by the creation of calcium ions (as ionic crosslinking takes place).
Compressive creep strain plot. Taken from [1]
0.09 kPa
0.77 kPa
0.41 kPa
4.61 kPa
10.67 kPa

## Slide 5: Conclusions:
Literature demonstrates that Gel-Alg obtained its viscoelastic strain and elastic recovery properties and can be potentially used to design extracellular matrix mimicking hydrogels.

## Slide 7: Creep test
  Pure GelMA
    0.49% viscoelastic strain (5 min)
  GelMA-Alginate composite (50/50 Gel-Alg)
    viscoelastic stain: 6.9% (2% alginate)
    viscoelastic stain: 10% (5% alginate)
  The viscoelastic strain of Gel-Alg composite decreases with decreasing amounts of alginate
    viscoelastic stain: 7.33% (50:50 GelMA: Alginate)
    viscoelastic stain: 3.73% (65:35 GelMA: Alginate)
    viscoelastic stain: 3.46% (80:20 GelMA: Alginate)
    viscoelastic stain: 2.85% (100:0 GelMA: Alginate)
[1] Y. X. Chen, B. Cain, P. Soman, Gelatin methacrylate-alginate hydrogel with tunable viscoelastic properties, AIMS Mater. Sci. 4 (2017) 363–369. https://doi.org/10.3934/matersci.2017.2.363.
Purely covalently UV-crosslinked GelMA results in a predominantly elastic material